# Design description
## General remarks
- Offsets & lengths in bytes.
- The VFS is organized in blocks with fixed BLOCK_SIZE.
- All addresses are in number of blocks from 0 and of length 4 bytes.
- Only single links to blocks (not more than one hard-link) are allowed. This means that one file or directory can only be in one directory.
- Block address 0 is illegal, it means absence of a block.
## Metadata
Metadata of the whole VFS starts at address 0.
Offset (absolute)	Length	C# data-type	Description
0	4	UInt32	Number of blocks in entire VFS
4	4	UInt32	BLOCK_SIZE in bytes
8	4	UInt32	Address of root directory node
12	4	UInt32	Address of empty page block. Must never be 0.
16	4	UInt32	“break” in number of blocks, see empty space management.
20	Blocksize -20	UInt32	Empty (initialized with 0)

## Blocks
Normal blocks are everywhere but at address 0.
### Block types
- Directory blocks (many different blocks, with optional continuation blocks)
- File blocks (many different blocks, with optional continuation blocks)
- Data blocks (many different blocks)
- Empty space block (exactly one block, with optional continuation blocks)
### Directory blocks
Contain file / directory names of current directory and their block addresses.
Offset (relative)	Length	C# data-type	Description
0	?	-	Arbitrary number of directory entries
BLOCK_SIZE – 4	4	UInt32	Link to directory continuation block. 0 here marks absence of continuation blocks.

Directory continuation blocks look the same as directory blocks and can link to other directory continuation blocks.
#### Directory entry
Offset (relative)	Length	C# data-type	Description
0	1	UInt8 = byte	If first bit (the least significant) set (== 1), following address points to directory. Else to file.
2	1	UInt8 = byte	Number of bytes in file name. 0 here marks end of directory block.
3	X	String encoded in UTF-8	File / directory name
X	X + 4	UInt32	Address to file / directory block

### File blocks
Contain addresses to data blocks.
Offset (relative)	Length	C# data-type	Description
0	8	UInt64	File size in bytes (to manage files smaller than block size)
8	?	UInt32	Arbitrary number of addresses to data blocks
BLOCK_SIZE – 4	4	UInt32	Link to file continuation block. 0 here marks absence of continuation blocks.

File continuation blocks have file size 0 and can link to other file continuation blocks.
### Data blocks
Contain only plain binary data.
### Empty space block
Contains addresses to empty blocks.
Offset (relative)	Length	C# data-type	Description
0	4	UInt32	Number of empty blocks in number of blocks
4	?	UInt32	Arbitrary number of addresses to empty blocks
BLOCK_SIZE – 4	4	UInt32	Link to empty space continuation block. 0 here marks absence of continuation blocks.

## Empty space management
The VFS is designed to maintain an index of unused blocks. The addresses of the unused blocks are stored in the empty space block. Its address is stored in the VFS meta-data. This empty space block may also have empty space continuation blocks. But not every address to an empty block in the whole VFS can be stored in this empty space block. Instead, only addresses of empty blocks up to a maximum address, which is called “break”, is stored in this block. If there are no empty blocks left, the “break” must be increased by 1, and the new empty block addresses must be added to the empty space block. If the block next to “break” is freed, decrease the “break”, otherwise the address of this block to the empty space block or its last continuation block.